# New MEYLE-HD tie rod ends for Dacia models

- Technically refined suspension parts to fit Dacia Logan and Sandero models

- High-performance grease specially geared to MEYLE parts prevents stick/slip

- Extended four-year warranty thanks to extra long service life

Hamburg, 21 July 2015. As of now, independent workshops can offer customers an extended four-year warranty period on yet another replacement part: Under its MEYLE-HD brand Wulf Gaertner Autoparts AG now also supplies a technically refined tie rod end to fit Dacia Lagan and Sandero models. Subject to excessively high loads, tie rod end assemblies are destined to wear out quickly. Relying on the high-strength MEYLE solution allows repair professionals to offer premium-grade repairs and build strong customer relations.

Tie rod end assemblies are exposed to continually high levels of strain. Steering while stationary applies high radial forces on the tie rod end, while bumpy roads take an additional toll, often resulting in premature part wear, typically manifesting itself in the form of noise and steering play. The new MEYLE-HD tie rod end for Dacia models features a larger ball head than typically found on conventional designs, which allows forces acting on the ball to be distributed more effectively thereby reducing the surface pressure applied on the ball joint's plastic socket.

Additionally, the specially formulated MEYLE lubricant is optimally geared to the materials making up the joint, i.e. steel, plastics and rubber. Designed in collaboration with a specialist manufacturer of high-performance greases, the MEYLE lubricant helps minimise stick/slip and breakaway torque. Under all operating conditions, the grease provides for a constant lubricant film between the ball pin and plastic socket, thereby ensuring smooth movement in the ball joint.

All these technical refinements combine to deliver a part which lasts considerably longer than its original equipment equivalent. The new MEYLE-HD tie rod ends for the Dacia Logan and Sandero are available under the MEYLE part numbers 16-16 020 0011/HD and 16-16 020 0012/HD. As with all products of the MEYLE-HD range, Wulf Gaertner Autoparts also gives a full four-year warranty on these HD tie rod ends.

Download our press releases and press pictures from www.meyle.com or order in electronic file format.

Contact:

- Public Relations von Hoyningen-Huene, Marc von Bandemer, phone: +49 40 416208-17, e-mail: mvb@prvhh.de

- Wulf Gaertner Autoparts AG, Annika Fuchs, phone: +49 40 67506-519, E-Mail: annika.fuchs@meyle.com

About the Company

Wulf Gaertner Autoparts AG develops, produces and sells top-quality and quality-certified spare parts for cars, vans and trucks for the independent aftermarket under the brands of MEYLE and MEYLE-HD. The Hamburg manufacturer’s portfolio currently includes more than 18,500 articles, covering practically every requirement on the market. Engineers at the company also focus on products and services which can improve processes within the workshop. The MEYLE engineers have developed around 750 parts for thousands of different vehicle models and have technically optimised such parts compared to those made by the original equipment manufacturers. These MEYLE-HD products are extremely resilient and have a long service life. There is a four-year warranty on the unique feature of technically improved MEYLE-HD parts.

Wulf Gaertner Autoparts AG was founded in 1958 and is headquartered in Hamburg, Germany. The company operates in 120 countries. In addition to its state-of-the-art logistics centre in Hamburg, the company also operates subsidiaries and production sites worldwide.