The "MEYLE Mechanics" advice: One universally designed MEYLE-HD BMW control arm fits three different original designs

- Latest video on "MEYLE TV" shows how to maximise repair-time efficiency by dispensing with time-consuming initial wheel alignment measurement

- Latest product range addition: MEYLE-HD control arm kit for BMW 5 (F10, F11) and BMW 6 (F12, F13) series models

Hamburg, 11 August 2015. Committed to helping workshops streamline repair routine, the "MEYLE Mechanics" have dedicated their latest video to control arm repair on BMW 5, 6 and 7 Series models explaining in detail how MEYLE-HD kits help make repairs compellingly simple and time-effective and why initial wheel alignment measurement is no longer required.

The “MEYLE TV” YouTube channel features a range of instructional "MEYLE Mechanics" videos providing tips and tricks on how to increase repair-time efficiency and cost effectiveness. The latest video spotlights control arm assembly on BMW 5, 6 and 7 series models – an often cumbersome task, as identifying the correct control arm requires an initial wheel alignment measurement. Here is the link to the latest video: https://youtu.be/QK6PikkkYZs.

Thanks to the variably adjustable ball joint, the MEYLE-HD control arm design is suitable for three different OE versions. In the video, the "MEYLE Mechanics" guide repair professionals through the installation procedure, from mounting the MEYLE-HD control arm in zero position to setting it to positive or negative following axle alignment. The MEYLE design bears tremendous time saving potential during both installation and ordering, as one universally engineered part fits several different vehicle applications.

To extend control arm life beyond that of its OE counterpart the Hamburg company's team of in-house engineers has also refined some of its technical specifications: For example, the ball joint of the control arm features a highly resistant anti-corrosion coating and the socket is made from extremely abrasion-resistant plastic material. Owing to the technical improvements over the OE design, the BMW control arm (MEYLE no. 316 050 0044/HD), as all items of the MEYLE-HD range, comes with a full four-year warranty.

The new control arm kit caters for BMW 5 (F10, F11) and BMW 6 (F12, F13) Series models and contains all parts required for repair including the mounting material, and is now available under the MEYLE no. 316 050 0080/HD.

Download our press releases and press pictures from www.meyle.com or order in electronic file format.

Contact:

- Public Relations von Hoyningen-Huene, Marc von Bandemer, phone: +49 40 416208-17, email: mvb@prvhh.de

- Wulf Gaertner Autoparts AG, Annika Fuchs, phone: +49 40 67506-519, email: annika.fuchs@meyle.com

About the Company

Wulf Gaertner Autoparts AG develops, produces and sells top-quality and quality-certified spare parts for cars, vans and trucks for the independent aftermarket under the brands of MEYLE and MEYLE-HD. The Hamburg manufacturer’s portfolio currently includes more than 18,500 articles, covering practically every requirement on the market. Engineers at the company also focus on products and services which can improve processes within the workshop. The MEYLE engineers have developed around 750 parts for thousands of different vehicle models and have technically optimised such parts compared to those made by the original equipment manufacturers. These MEYLE-HD products are extremely resilient and have a long service life. There is a four-year warranty on the unique feature of technically improved MEYLE-HD parts.

Wulf Gaertner Autoparts AG was founded in 1958 and is headquartered in Hamburg, Germany. The company operates in 120 countries. In addition to its state-of-the-art logistics centre in Hamburg, the company also operates subsidiaries and production sites worldwide.