Learn from the "MEYLE Mechanics" how to diagnose a defective transmission mount

New Workshop Advice on the "MEYLE TV" YouTube channel: Video

Hamburg, 10 May 2016. Exposed to excessive vibration and high load levels during drive-off and gear shift, transmission mounts are prone to wear out quickly, thus requiring frequent replacement. Therefore, repair professionals are well advised to perform a transmission mount functional check as part of their repair routine. Whether or not the mounts require replacement can be assessed by visual inspection and/or checking for noise. In their latest YouTube video on "MEYLE TV" the "MEYLE Mechanics" explain how to pinpoint a defective transmission mount and why it should be replaced.

Using the MEYLE-HD transmission mount (MEYLE ref. 014 024 1100/HD) to fit Mercedes-Benz C-, CLK-, CLS-, E-, G-, S-, SL- and SLK-Class models they also demonstrate the part's operational principle. The special feature about this part: Unlike OE designs where different components must be used depending on the engine type, the engineering team of German manufacturer Wulf Gaertner Autoparts has devised a stronger design to make the MEYLE-HD transmission mount suitable for use in a number of different vehicle models: This means that workshops using the new MEYLE-HD transmission mount only need one type of spare part to offer repair services for several different types of car models. Offering a highly compact design, the part features a carefully formulated rubber material engineered to absorb vibration even better. This way, transmission mount life is significantly increased which is why the part comes with an extended four-year guarantee, as do all items of the MEYLE-HD range. The reinforced design also makes this MEYLE-HD part a smart option for taxi fleet operators.

To watch the new transmission mount video, follow this link: https://youtu.be/6qFaR7dcrUM.

Download our press releases and press pictures from www.meyle.com or order in electronic file format.

Contact:

- Public Relations von Hoyningen-Huene, Marc von Bandemer, phone: +49 40 416208-17, e-mail: mvb@prvhh.de

- Wulf Gaertner Autoparts AG, Annika Fuchs, phone: +49 40 67506-519, E-Mail: annika.fuchs@meyle.com

About the Company

Wulf Gaertner Autoparts AG develops, produces and sells top-quality and quality-certified spare parts for cars, vans and trucks for the independent aftermarket under the brands of MEYLE and MEYLE-HD. The Hamburg manufacturer’s portfolio currently includes more than 21,000 articles, covering practically every requirement on the market. Engineers at the company also focus on products and services which can improve processes within the workshop. The MEYLE engineers have developed around 750 parts for thousands of different vehicle models and have technically optimised such parts compared to those made by the original equipment manufacturers. These MEYLE-HD products are extremely resilient and have a long service life. There is a four-year guarantee on the unique feature of technically improved MEYLE-HD parts.

Wulf Gaertner Autoparts AG was founded in 1958 and is headquartered in Hamburg, Germany. The company operates in 120 countries. In addition to its state-of-the-art logistics centre in Hamburg, the company also operates subsidiaries and production sites worldwide.